## Slide 1: SYSTEM UNIT CPU & MAIN MEMORY

## Slide 2: System unit
System unit is a case that contains electronic components of the computer used to process data.
The system unit houses
  the motherboard (including the processor chip and memory chips),
  the power supply, and
  storage devices.
  The system unit includes: a motherboard, processor, memory module, cards, ports and connectors.
Also called the case or system cabinet, chasis
System unit – is the interior views of the box, or case.
The case of the system unit is made of metal or plastic and protects the internal electronic components from damage.
The arrangement of the components varies among models.

## Slide 3: 1. The motherboard
Motherboard, or system board, is the main circuit board in the system unit.
Motherboard consists of a flat board that fills one side of the case.
It contains both soldered, non removable components and sockets or slots for components that can be removed—microprocessor chip, RAM chips, and various expansion cards.
Many integrated circuits are etched on it.
Each IC (integrated circuit) contains millions of transistors which act as switches for electronic signals.

## Slide 4
THE MICROPROCESSOR CHIP
Motherboard may be thought of as your computer’s central nervous system.
The brain of your computer is the microprocessor chip.
It stores program instructions that process, or manipulate, data into information.
  A chip, or microchip, is a tiny piece of silicon that contains millions of microminiature integrated electronic circuits
  A circuit is a closed path followed or capable of being followed by an electric current.

## Slide 5
Transistors—key parts of a chip:
The key parts of the microprocessor are transistors.
Transistors are tiny electronic devices that act as on/off switches, which process the on/off (1/0) bits used to represent data.
Chipset—chips for controlling information among system components:
Chipset consists of groups of interconnected chips on the motherboard that control the flow of information between the microprocessor and other system components connected to the motherboard.
The chipset determines what types of processors, memory, and video card ports will work on the same motherboard.
It also establishes the types of multimedia, storage, network, and other hardware the motherboard supports.

## Slide 6
CPU- Central Processing Unit
Most PCs use CPUs manufactured by Intel Corporation or Advanced Micro Devices (AMD).
They currently fall into three groups:
1. Intel Pentium series and Intel Celeron series
2. Equivalent processors, such as AMD Athlon series.
3. Apple G series.
Microsoft Windows operating system was designed to run on Intel chips.
The speed of a processor is measured in Hertz (Hz) where 1 Hz = 1 cycle per second.
This refers to fetch execution cycle, which is the process of copying one program instruction from the main memory then carry out the instruction.
Today’s processors can carry out many instructions per second.
Hence the speed is measured in MHz (Megahertz) or GHz (Gigahertz).

## Slide 7
PARTS OF THE CPU
A processor is also called CPU, and it works hand in hand with other circuits such as main memory to carry out processing.
CPU (central processing unit) is the “brain” of the computer;
it follows the instructions of the software (program) to manipulate data into information.
Impacts on the overall computing power and manages most of the computer operations.
CPU consists of two parts—
  (1) the Control Unit and (CU)
  (2) the Arithmetic/logic unit (ALU),
  contain registers, or high-speed storage
  All are linked by an electronic “roadway” called a bus.

## Slide 8
1. Control unit—for directing electronic signals:
Control unit deciphers each instruction stored in the CPU and then carries out the instruction.
Directs and coordinates most of the operations in a computer
It directs the movement of electronic signals between main memory and the arithmetic/logic unit.
It also directs these electronic signals between main memory and the input and output devices.

## Slide 9
For every instruction, the Control Unit carries out four basic operations, known as the machine cycle.
In the machine cycle, the CPU
  (1) fetches an instruction or data item from the memory,
  (2) decodes the instruction into a command a computer can understand,
  (3) executes the instruction or command, and
  (4) stores or write the results to the memory.

## Slide 10
In some computers, the processor fetches, decodes, executes, and stores only one instruction at a time.
In these computers, the processor waits until an instruction completes all four stages of the machine cycle (fetch, decode, execute, and store) before beginning work on the next instruction.
Most of today’s personal computers support a concept called pipelining.
With pipelining, the processor begins fetching a second instruction before it completes the machine cycle for the first instruction.
Processors that use pipelining are faster because they do not have to wait for one instruction to complete the machine cycle before fetching the next.

## Slide 11
2. The arithmetic/logic unit— for arithmetic and logical operations:
ALU - performs arithmetic operations and logical operations and controls the speed of those operations.
Arithmetic operations are major math operations: addition, subtraction, multiplication, and division.
Logical operations are comparisons.
That is, ALU compares two pieces of data to see whether one is equal to (=), greater than (>), greater than or equal to (>=), less than (<), less than or equal to (<=), or not equal to (≠) the other.
ALU - Performs the execution part of the machine cycle.

## Slide 12
Registers—small high-speed storage areas that temporarily store data during processing.
Control Unit and the ALU also use registers, Registers enhance the computer’s performance.
Registers are part of the processor, not part of memory or a permanent storage device.
There are different types of registers each with a specific storage function.
Register functions include storing the location from where an instruction was fetched, storing an instruction while the control unit decodes it, storing data while the ALU computes it, and storing the results of a calculation.
There are several types of registers, including instruction register, address register, storage register, and accumulator register.

## Slide 13
All data must be represented in a register before it can be processed.
E.g. if two numbers are to be multiplied, both numbers must be in registers, and the result is also placed in a register.

## Slide 14: Processor Cooling
Processor chips generate a lot of heat, which could cause the chip to burn up.
Because of that, computers has a fan that generates airflow but the processors require additional cooling.
Heat sinks/ pipes and liquid cooling technologies often are used to help dissipate (drive away, disolve, dispel) processor heat.
A heat sink is a small ceramic or metal component with fins on its surface that absorbs and disperses heat produced by electrical components such as a processor

## Slide 15
Some heat sinks are packaged as part of a processor chip.
Others are installed on the top or the side of the processor chip.
Because a heat sink consumes extra space, a smaller device called a heat pipe cools processors in notebook computers, including netbooks and Tablet PCs.
Some computers use liquid cooling technology to reduce the temperature of a processor.
Liquid cooling technology uses a continuous flow of fluid(s), such as water and glycol, in a process that transfers the heated fluid away from the

## Slide 16
Buses
Buses or bus lines, are electrical data roadways through which bits are transmitted within the CPU and between the CPU and other components of the motherboard.
A bus is a data path between several hardware components inside or outside a computer.
It connects parts of a CPU and other hardware.
The capacity is expressed in bits
The larger the bus the faster, for example, a 32 bit bus is faster than 8 bit bus.
A bus resembles a multilane highway:
The more lanes it has, the faster the bits can be transferred.
  A bit is the smallest unit of information used by computers.
  data transmission speeds are measured in bits, kilobits, megabits, and gigabits per second
8-bit-word bus of early microprocessors had only eight pathways.
Data is transmitted four times faster in a computer with a 32-bit bus, which has 32 pathways, than in a computer with an 8-bit bus.
Supercomputers have 128-bit processors.
There are three main bus architectures:

## Slide 17
a. ISA (Industrial Standard Architecture)
This is the original PC bus architecture
It includes 8 bit (PC, XT) and 16 bit (AT) buses in IBM personal computer series and compatibles.
Now it refers to 16 bit AT bus.
b. MCA (Micro Channel Architecture)
A 32 bit bus used in IBM P/S 2 series and other IBM modules.
This architecture allows multiprocessing that allows several processors to work simultaneously.
MCA is not compatible with PC bus architecture.
c. EISA (Extended Industrial Standard Architecture)
Extends AT bus (ISA) architecture to 32 bit bus.
It allows more than one CPU to share the bus.
Extends and amends the old ISA standard so that the existing AT expansion board can work with an EISA slot

## Slide 18: 4. Expansion Slots and Adapter Cards
An expansion slot is a socket or an opening on the motherboard that can hold an adapter card.
An expansion slot is an opening or a socket where you can insert circuit boards into motherboard.
An adapter card, sometimes called an expansion card, is a circuit board that enhances functions of a component of the system unit and/or provides connections to peripherals.
These circuit boards called cards, expansion cards, boards, expansion boards, adapters, adapter cards; interface cards, add-ins or add-ons add new devices or capabilities to a computer.
Four types of expansion cards found in computers are: video card, sound card, network interface card and modem card.

## Slide 19
Types Of Expansion Cards
Graphics cards—for monitors: Graphics cards are included in all PCs.
Also called a video card, video RAM (VRAM), or video adapter, a graphics card converts signals from the computer into video signals that can be displayed as images on a monitor.
Sound cards—for speakers and audio output: A sound card is used to convert and transmit digital sounds through analog speakers, microphones, and headsets.
Modem cards—for remote communication via phone lines.
Network interface cards—for remote communication via cable: A network interface card (NIC) allows the transmission of data over a cable network.
PC cards—for laptop computers: Originally called PCMCIA cards (for the Personal Computer Memory Card International Association),
PC cards are thin, credit card–size flash memory devices used principally on laptop computers to expand capabilities, such as to access the internet wirelessly.

## Slide 20: 5. Ports
A port is an external connecting socket on the outside of the computer.
This is a pathway into and out of a computer.
A port lets users plug in outside peripherals such as monitors, scanners and printers.
There are two types of ports:

## Slide 21
a. Serial ports
External I/O connector used to attach modems, scanners or other serial interface devices to the computer.
They typically use a 9 pin DB-9 or a 25 pin DB-25 connectors.
Serial lines are used to link equipment that is not located close by.
b. Parallel Ports
External I/O connectors used to hook up printers and other parallel interface devices.
It transmits several bits simultaneously.
Moves information faster than serial.

## Slide 22
Memory
Memory consists of electronic components that store instructions waiting to be executed by the processor, data needed by those instructions, and the results of processing the data (information).
This is a temporary storage of data, instructions and information
Memory stores three basic categories of data:
  (1) the operating system and other system software that control or maintain the computer and its devices;
  (2) application programs that carry out a specific task such as word processing; and
  (3) the data being processed by the application programs and resulting information.
  This role of memory to store both data and programs is known as the stored program concept.
  A byte (character) is the basic storage unit in memory.
  A group of 8 bits is called a byte.
  1 byte can store one alphabetical letter, single digit or single character symbol such as #.
  Large number of bytes can be expressed in kilobytes and megabytes.

## Slide 23
Types of Memory
The system unit contains two types of memory:
  volatile and nonvolatile.
When the computer’s power is turned off, volatile memory loses its contents.
Nonvolatile memory does not lose its contents when power is removed from the computer.
Therefore, volatile memory is temporary and nonvolatile memory is permanent.
RAM is the most common type of volatile memory.
Examples of nonvolatile memory include ROM, flash memory, and CMOS.
The following sections discuss these types of memory.

## Slide 24
RAM (random access memory) chips
  temporarily hold (1) software instructions and (2) data before and after it is processed by the CPU.
Think of RAM as the primary workspace inside your computer.
When you open a file, a copy of the file transfers from the hard disk to RAM, and this copy in RAM is the one that changes as you work with the file.
When you activate the Save command, the changed copy transfers from RAM back to permanent storage on the hard drive.
Because its contents are temporary, RAM is said to be volatile —the contents are lost when the power goes off or is turned off.
This is why you should frequently —every 5–10 minutes, —transfer (save) your work to a secondary storage medium such as your hard disk, in case the electricity goes off while you’re working.
Saving is the process of copying data, instructions, and information from RAM to a storage device such as a hard disk.

## Slide 25
Several types of RAM chips are used in personal computers—
  DRAM: (pronounced “dee-ram”), DRAM (dynamic RAM), must be constantly refreshed or re-energized by the CPU or it will lose its contents.
  SDRAM: (synchronous dynamic RAM), which is synchronized by the system clock and is much faster than DRAM.
  SRAM: static RAM, or SRAM is faster than DRAM and retains its contents without having to be refreshed by the CPU.
  DDR-SDRAM: (double-data rate synchronous dynamic RAM), is the current standard of RAM chip in PCs used at home;
  the speed is measured in megahertz.
  A faster version is DDR2 SDRAM, which is found on gaming machines and multimedia machines, where speed is needed.

## Slide 26
Microcomputers come with different amounts of RAM, which is measured in megabytes or gigabytes.
The more RAM you have, the more efficiently the computer operates and the better your software performs.
Before you buy a software package, check how much RAM is required.
  E.g. Windows7, Vista requires 512 megabytes to 1 gigabyte minimum RAM

## Slide 27
RAM chips reside on a memory module.
Memory slots on the motherboard hold memory modules.
Three types of memory modules are SIMMs,
DIMMs, and RIMMs. A SIMM (single inline memory module) has pins on opposite sides of the circuit board that connect together to form a single set of contacts.
With a DIMM (dual inline memory module), the pins on opposite sides of the circuit board do not connect and thus form two sets of contacts.
SIMMs and DIMMs hold SDRAM chips.
A RIMM (Rambus inline memory module) houses RDRAM chips.

## Slide 28
If you’re short on memory capacity, you can add more RAM chips by plugging a RAM memory module into the motherboard.
A memory module is a small fiberglass circuit board that can be plugged into an expansion slot on the motherboard.
  A circuit is a closed path followed or capable of being followed by an electric current.
There are two types of memory modules:
  SIMMs and the newer DIMMs.
  SIMM: A SIMM (single inline memory module) has RAM chips on only one side.
  SIMMs are available in either FPM (fast page mode) or EDO (extended data output) speeds, with EDO being the faster of the two.
  SIMMs are more expensive than modern memory modules because they are no longer in demand, which also makes them difficult to obtain.
  DIMM: A DIMM (dual inline memory module) has RAM chips on both sides.
DIMMs are the most popular and common type of RAM used today.

## Slide 29
ROM Chips—to Store Fixed Start-up Instructions
Read-only memory (ROM) stores information that can only be read and not modified.
Modifying it is either impossible or very difficult.
ROM is a type of non-volatile storage, which means that the information is maintained even if the component loses power.
In a computer system, ROM is located on the motherboard.
It contains basic instructions for what needs to happen when a computer is powered on.
ROM (read-only memory) cannot be written on or erased by computer user without special equipment.
Memory that can only be read i.e. it cannot be modified.
ROM chips are loaded, at the factory, with programs containing special instructions for basic computer operations, such as those that start the computer (BIOS) or put characters on the screen.
ROM plays a critical part in starting up your computer. This is also referred to as booting up your computer.

## Slide 30
In computer terminology, read means to transfer data from an input source into the computer’s memory or CPU.
The opposite is write —to transfer data from the computer’s CPU or memory to an output device.
ROM, read-only means that the CPU can retrieve programs from the ROM chip but cannot modify or add to those programs.
A variation is PROM (programmable read-only memory), which is a ROM chip that allows the user, to load read-only programs and data, this can be done only once.
A variation of the PROM chip, called an EEPROM (electrically erasable programmable read-only memory) chip, allows a programmer to erase the microcode with an electric signal.

## Slide 31
CMOS Chips— Pronounced´“ see -moss,”
CMOS (complementary metal-oxide semiconductor) chips are powered by a battery therefore don’t lose their contents when the power is turned off.
CMOS chips contain flexible start-up instructions—such as time, date, and calendar—that must be kept current even when the computer is turned off.
CMOS chips can be reprogrammed when you need to change the time for daylight savings time.
Memory chip that stores configuration information of a computer.
Uses battery power to retain the information when the computer is switched off.

## Slide 32
FLASH MEMORY
Flash memory is a type of nonvolatile memory that can be erased electronically and rewritten, similar to EEPROM.
A nonvolatile form of memory, flash memory chips can be erased and reprogrammed more than once
  (unlike PROM chips, which can be programmed only once).
Flash memory doesn’t require a battery and can range from 128 megabytes to 32 gigabytes and up in capacity,
Flash memory chips also store data and programs on many mobile computers and devices, such as smart phones, portable media players, PDAs, printers, digital cameras, automotive devices, digital voice recorders, and pagers.
Flash memory is an electronic non-volatile computer storage medium that can be electrically erased and reprogrammed.
When you enter names and addresses in a smart phone or PDA, a flash memory chip stores the data.
Some portable media players store music on flash memory chips (Figure 4-23); others store music on tiny hard disks or flash memory cards.
Flash memory cards contain flash memory on a removable device instead of a chip.

## Slide 33
Removable Flash Memory
Removable flash memory includes memory cards, USB flash drives, and PC Cards/ExpressCard module.
A memory card is a removable flash memory device, usually no bigger than 1.5" in height or width, that you insert and remove from a slot in a personal computer, game console, mobile device, or card reader/writer

## Slide 34
Cache (pronounced as cash)
Cache temporarily stores instructions and data that the processor is likely to use frequently.
Memory cache help to speed the processes of the computer because it stores frequently used
Cache speeds up processing, improves processing time because it stores frequently used instructions or data.
Most personal computers today have two types of memory cache: L1 cache and L2 cache. Some also have L3 cache.
SRAM chips are commonly used for cache.
computers improve their processing times with cache.

## Slide 35: Power Supply
Electricity from a wall outlet is alternating current (AC) of 115 to 120 volts, but a microcomputer runs on direct current (DC) ranging from 5 to more than 15 volts.
  DC - electrical current which moves in one direction only.
  AC - electrical current which regularly changes the direction in which it moves .
Power supply is a device that converts AC to DC to run the computer.
The power supply is the component of the system unit that converts the wall outlet AC power into DC power.
Because electricity can generate a lot of heat, a fan inside the computer keeps the power supply and other components from becoming too hot.
Electrical power drawn from a standard AC outlet can be quite uneven.
For example, a sudden surge, or “spike,” in AC voltage can burn out the low-voltage DC circuitry in your computer (“fry the motherboard”).
Instead of plugging your computer directly into a wall electrical outlet, it’s a good idea to plug it into a power protection device.
The three principal types are surge protectors, voltage regulators, and UPS units.
  UPS (uninterruptible power supply)

## Slide 36
Different motherboards and computers require different wattages on the power supply.
Notebook computers, and Tablet PCs, can run using either batteries or a power supply.
If a power supply is not providing the necessary power, the computer will not function properly.
Built into the power supply is a fan that keeps the power supply cool.
Some have variable speed fans that change speed or stop running, depending on temperature in the system unit

## Slide 37
Port and connectors
A port is an external connecting socket on the outside of the computer.
This is a pathway into and out of a computer.
A port lets users plug in outside peripherals such as monitors, scanners and printers.
A port is the point at which a peripheral attaches to or communicates with a system unit so that the peripheral can send data to or receive information from the computer.
An external device, such as a keyboard, monitor, printer, mouse, and microphone, often attaches by a cable to a port on the system unit.
Instead of port, the term jack sometimes is used to identify audio and video ports.
The front and back of a system unit on a desktop personal computer contain many ports.
On notebook computers, including netbooks and Tablet PCs, the ports are on the back, front, and/or side.

## Slide 38
There are two types of ports:
  a. Serial ports
    External I/O connector used to attach modems, scanners or other serial interface devices to the computer.
    They typically use a 9 pin DB-9 or a 25 pin DB-25 connectors.
    Serial lines are used to link equipment that is not located close by.
  b. Parallel Ports
  External I/O connectors used to hook up printers and other parallel interface devices.
  It transmits several bits simultaneously.
  Moves information faster than serial.

## Slide 39
A connector joins a cable to a port. A connector at one end of a cable attaches to a port on the the cable attaches to a port on the peripheral.
Most connectors and ports are available in one of two genders: male or female.
Male connectors and ports have one or more exposed pins, like the end of an electrical cord you plug in the wall.
Female connectors and ports have matching holes to accept the pins on a male connector or port, like an electrical wall outlet.

## Slide 40
Sometimes, you cannot attach a new peripheral to the computer because the port on the system unit is the same gender as the connector on the cable.
In this case, purchasing a gender changer solves this problem.
A gender changer is a device that enables you to join a port and a connector that are both female or both male.

## Slide 41
Bays
A bay is an opening inside the system unit in which you can install additional equipment.
A bay is different from a slot on the motherboard, which is used for the installation of adapter cards.
A drive bay is a rectangular opening that typically holds disk drives.
Other bays house card readers and widely used ports such as USB, FireWire, and audio ports.
An external bay allows a user to access openings in the bay from outside the system unit.
Optical disc drives are examples of devices installed in external bays.
An internal bay is concealed entirely within the system unit.
Hard disk drives are installed in internal bays.